## Slide 1: 8D Problem Solving Methodology Problem –Ball depth observed under size up to 8.32, against 8.7 ± 0.1 Supplier Name- Cast 4 Aluminium ltd Part Name- SECONDARY LEVER FINISHE ATHER DISC DRUM.

## Slide 2: 8D - Overview
Supplier Name : Cast 4 Aluminium Ltd.
D1: Problem Solving Team :
Mahesh Ghadmode
Datta Moin
Mubarak Shaikh
Solving Team Leader: Mr. Mahesh Ghadmode
Problem Sub Suppliers Team members:
Endurance Team Members:
Format No.:QLQL_FMT_007 Rev-00 Effective Date:29-09-2022

## Slide 3: 8D - Overview
D2 :Problem description details (with Pictures)
(Clearly mention what is the defect found at Ather & what is the deviation found in the part with respect to the drawing requirements)
 | Details
What | Ball depth observed under size up to 8.32, against 8.7 ± 0.1
Where | ETL
When | 26-10-2024
Who | Mahesh Ghadmode
How Much | 01 no’s
Problem Description in 4W 1H
NG Photograph

## Slide 4: 8D - Overview
D3 : Immediate Containment action (ICA):
Notes:
1. Clearly mention ICA Action and identification mark after ICA
2. ICA to be in place at supplier end of line till D7 effectiveness
Stocks | Description of Action | Sorting results |  | Resp. | Target Date | Quantitative assessment in %
 |  | How many checked | How many failed |  |  | 
IQC | - | - | - | - | - | 
Ather Store Stock |  |  |  |  |  | 
In Transit ( At WH) |  |  |  |  |  | 
At Supplier | 535 | 535 | 05 | Vishwas Borkar | 28-10-2024 | 
Endurance Spares | NA | NA | NA | NA | NA | NA

## Slide 5
Approved by : R.Magar
Part Name : Secondary brake lever Ather Dnd | Operation Details : VMC Machining
Process Deviation details with Photograph: | Check points & Identification mark wrt ICA :
QUALITY ALERT
Prepared By : Mahesh Ghadmode
Not Ok
Ok
Date : 04.11.2023
Dot Marking at final inspection

## Slide 6: 8D - Overview
D4 : Root Cause Analysis (Occurrence)
D4.1: Mention all probable causes
Man
Machine/Die
Environment
Material
Method
Ball depth observed under size up to 8.32, against 8.7 ± 0.1
Measurement/Other
Unskilled operator
Lack of awareness
Hardness of part
Unspecified offset given by operator
Parts checked on sample basis
Interlock not available for offset
Clamping pressure drop
Resting not ok on fixture
Improper fettling

## Slide 7: 8D - Overview
Sr. No. | Ishikawa Category (6M) | Probable Causes Description | Significant / Insignificant | Validation reports Attachments
1 | Man | Unskilled operator | Significant | Skill matrix available of operator
2 | Man | Lack of awareness | Significant | Training record available
3 | Man | Unspecified offset given by operator | Significant | Interlock added to Offset Interface
4 | Machine | Clamping pressure drop | Significant | Power pack having provision to control pressure
5 | Machine | Resting not ok on fixture | Insignificant | As discussed with fixture manufacturer & provision will be implement to avoid parting line resting
6 | Material | Hardness of part | Significant | Hardness of material check found ok
7 | Material | Improper fettling | Significant | Fettling SOP available at respective location
8 | Measurement | Parts checked on sample basis | Significant | 100% inspection started with relation gauge
D4.2 : Validation of all Probable Causes : Ather Secondary Lever DnD

## Slide 8: 8D - Overview
D 4.3 : Why-Why Analysis:
Do Why-Why analysis for all validated significant potential causes
Why- Why Analysis for Occurrence Cause
WHY-1 | Ball depth observed under size up to 8.32, against 8.7 ± 0.1
WHY-2 | Part not rest in the fixture
WHY-3 | Part having excess parting line
WHY-4 | Parting line removal is manual operation
WHY-5 | No provision in fixture to avoid parting line
WHY-6 | 
Root Cause :No provision in fixture to avoid parting line
Why- Why Analysis for Detection Cause
WHY-1 | Ball depth observed under size up to 8.32, against 8.7 ± 0.1
WHY-2 | Parts checked on sample basis 5 Nos
WHY-3 | 100 % inspection started on relation gauge
Root Cause : Parts checked on sample basis 5 Nos

## Slide 9: 8D - Overview
Root cause | Occurrence/ Detection | Corrective action | Implementation date | Horizontal Deployment | Target Date for Horizontal Deployment
No provision in fixture to avoid parting line | Occurrence | As discussed with fixture manufacturer & provision will be implement to avoid parting line resting | 07.11.2024 | All VMC Machines | 15.11.2024
Parts checked on sample basis | Detection | 100% inspection started with the help of relation gauges | 28.10.2024 | All lever family | Completed
D5 & D6: Implementation of Corrective actions) : Ather Secondary Lever DnD

## Slide 10: 8D - Overview
D7: Updation of Preventive actions: List of the revised documents to attach
SN | Name | Doc. No. | Rev. No | Change Details | Attach revised Doc. here
1 | Design Record | - | - | - | -
2 | Engineering Change Documents (if any) | - | - | - | -
3 | Ather Engineering Approval (if required) | - | - | - | -
4 | Design FMEA | - | - | - | -
5 | Process Flow Diagram | - | - |  | -
6 | Process FMEA | F/DEV/13 | 02 | Dimple operation resting point added | 
7 | Control Plan | F/DEV/13 | 02 | Dimple inspection frequency change | Dimple inspection frequency change
8 | Measurement System Analysis Studies | - | - | - | -
9 | Dimensional Result | - | - | - | -
10 | Material, Performance Test Results | - | - | - | -
11 | Process Studies (Capability Study) | - | - | - | -

## Slide 11: 8D - Overview
Key Challenges:
D7 - Updation of Preventive actions (Standardization) :
D1 & D2 Bug Details:
D3 - Immediate Containment action (ICA):
D4 - Root Cause Analysis (Occurrence & Non-Detection)
D5 & D6 - Implementation of Corrective actions:
D8 Closure:
FMEA & CP, WI for Final Inspection,
Part No / Name : Secondary lever Ather DnD
Supplier : ETL
Swim lane :
Start date : Status (D) :
Problem Description : Ball depth observed under size up to 8.32, against 8.7 ± 0.1
Risk Level : High
For Occurrence:
No provision in fixture to avoid parting line
For Outflow:
Parts checked on sample basis 5 Nos
 | Ather IPQC | Ather Store Stock | ETL In Transit | At Supplier | ETL Spares
Inspected (Qty) | - | 0 | 600 | 535 | -
NG (Qty) | - | - | - | 5 | -
Action item | CA/PA | Target | Resp | Status
As discussed with fixture manufacturer & provision will be implement to avoid parting line resting | PA |  |  | 07.11.2024
100 % inspection started for dimple depth | PA |  |  | Completed
 | CA |  |  | In process

## Slide 12
No Provision available for resting parting line part

## Slide 13
As discussed with fixture manufacturer we will provide groove to the resting area to avoid parting line resting .

## Slide 14: Thank You
Format No.:QLQL_FMT_007 Rev-00 Effective Date:29-09-2022