## Slide 1
ACTIONS FOR ID OVER SIZE
Supplier: Saptagiri Industries.
Operation: Tube Cutting shop / Machine shop
Implementation Date: 10.09.2022
BEFORE
AFTER
Problem/Present Status: ID over size observed 28.4 against 28.0 + 0.1 mm
Material flow
Sampling inspection done only at receipt stage
‘’ Mandrel used at marking stage for tube guide
While cutting operation every length inspect by plane plug gauge.
At Receipt inspection sampling size increase
At CNC operation sampling stared to verify tube ID 28.0
RM Receipt
RM Inspection
Tube Cutting
Both side chamfer
CNC Machining
Forming
Marking
Buffing
At final inspection Q –Alert display
Awareness given to final inspector to ensure tube ID
Packing
Final Inspection
Ni. Cr. Plating
Material flow
RM Receipt
RM Inspection
Tube Cutting
Both side chamfer
CNC Machining
Forming
Marking
Buffing
Packing
Final Inspection
Ni. Cr. Plating
Sampling inspection done only at receipt stage | At Receipt inspection sampling size increase While cutting operation every length inspect by plane plug gauge. At CNC operation sampling stared to verify tube ID 28.0 ‘’ Mandrel used at marking stage for tube guide At final inspection Q –Alert display Awareness given to final inspector to ensure tube ID