## Slide 1
Burr observed at ending of thread Step mark on chamfer Chamfer angle more that is 55 degree against 45 degree Chamfer tool warn out | No burr on chamfer No Step mark on chamfer angle . Chamfer angle corrected as require 45 degree . Chamfer angle verified on profile projector Started 100% tapping inspection by TPG.
ACTIONS FOR NG THREADING (Hex NUT 520FL03012 )
Supplier: Saptagiri Industries.
Operation: Press shop / Machine shop
Implementation Date: 30.01.2023
BEFORE
AFTER
Problem/Present Status: GO not passing through out into the thread
Material flow
Burr observed at ending of thread
‘’ Chamfer tool replace with new one and started
Chamfer angle more that is 55 degree against 45 degree
Step mark on chamfer
No Step mark on chamfer angle .
No burr on chamfer
Chamfer angle corrected as require 45 degree
RM RECEIPT
Pressing
RM Inspection
Blanking
Both side chamfer
Plating
Threading
Packing
Final Inspection
RM RECEIPT
Pressing
RM Inspection
Blanking
Both side chamfer
Plating
Threading
Packing
Final Inspection
Material flow
Chamfer tool warn out
Chamfer angle verified on profile projector
Started 100% tapping inspection by TPG.